Packaging Guidelines

For Externally Purchased Parts

Vehicle Operations

Europe and Export

APRIL 2002

EU1750 	Materials, Planning and Logistics – Materials Handling and Packaging Engineering

Packaging Guidelines APRIL 2002

Contents:

PART  1:

General Requirements

PART 2 :

Vehicle Operations: European Packaging Requirements

PART 3 :

Export Operations:  Export Packaging Requirement

Appendices:

Appendix 1 - Glossary of Terms Appendix 2 - Packaging Data Input form Appendix 3 - Packaging Non Conformance Form Appendix 4 – Transport Mode Dimensions

Appendix 5 - Recycling & Plastics Identification Symbols

Appendix 6 - Durable Insert and Stretch Container Standard

PART 1

General Requirements

Applies to all European suppliers supplying components to Ford manufacturing locations, both in Europe and Export Locations.

Page

1.1	Introduction………………………………………………………….	3

1.2	Guidelines Application……………………………………………..	4

1.3	Supplier Responsibility…………………………………………….	5

1.4	Fords' Environmental Commitment………………………………	5

1.5	Lean Manufacturing……………………………….……………….	6

1.6	Packaging Approval Process……………………………………...	7

1.7	Database Update Process…………………………………………	7

1.7.1 New Model Programs……………………………………….	7

1.7.2 Current Models…………………………………………..…..	8

1.8	Approved Packaging Conformance Process…………………….	8

1.9	Continuous Improvement…………………………………………..	8

1.10	Final Check List……………………………………………………...	9

1.1 Introduction

These guidelines are to be used for all European sourced  PRODUCTION PARTS shipped to Ford European manufacturing plants, or to Ford Trading Companies for Export shipments.    The guidelines have been up-dated to re-enforce the policies laid out in the April 2000 issue, and reflect Fords' strategic packaging objectives, container selection process and operating procedures.

To summarise, these guidelines are in place to ensure the following:

Clarity of Ford packaging requirements for all European sourced material. Transparency of container and packaging material costs, which must be included in

all quotations.

Quality of the product to point of use

Support of  lean material flow by supplying parts to the production operator in the optimum sized standard container/IMC carton range

Containers are optimised for manual handling.  Gross weight must not exceed 12Kg for manually handled containers, and 313kg for FLC/FSC containers (if fork truck free delivery to line), or 563kg (FLC) and 543kg (FSC) (if items are to be fork trucked to the line).

Use of standard containers/IMC cartons specified in these guidelines wherever possible.  If they are not suitable for a particular product, the supplier will be required to  fund  100%  returnable  packaging  for  European  destinations,  or  an  agreed dedicated  carton  for  export  destinations  -  (authorisation  and  specification  to  be agreed individually with Ford MH&PE and Ford Purchasing)

Use of durable packaging and IMC cartons will optimise transport cube utilisation. Please note that different pallet bases are required for European shipments (metric

1200 x 1000), and Export Markets (Imperial 45" x 39" = 1140 x 980).   This is to

maximise freight cube for European trucks and trains, and ISO containers for export markets.

MH&PE  and  manufacturing  plant  packaging  contacts  are  provided  on  separate sheets, and will be updated and re-issued periodically.

Remember, the responsibility for ensuring component quality from your plant to the point of use remains with you - the supplier of the product.

1.2 Guidelines Application

Packaging Guidelines January 2002 now incorporate both European domestic and export packaging requirements, and are applicable for all components shipped from European suppliers to the following locations:

PART 2 - European Manufacturing plants

Use Durable Packaging for:

| 0134A 0096A | Cologne Genk | Body and Assembly Operations Body and Assembly Operations |
| --- | --- | --- |
| 0097A | Saarlouis | Body and Assembly Operations |
| 0145A 0118A 0116A | Valencia Southampton Croydon | Body and Assembly Operations Body and Assembly Operations Stamping Operations |
| 0119A | Dagenham | Stamping Operations |

PART 3 – Export operations through the following Ford Trading Companies

Use Export Packaging for:

| 0134D, 0134F, 0134T, 0134H 0134R, 0134U | Brazil, Argentina Mexico, South Africa | P. Huppertz |
| --- | --- | --- |
| 0142S, 0142T, 0142W, AYFUA | Turkey, Taiwan, Russia |  |
| 0134E, 0134G, 0134L 0134Q, 01420, 0142U | Brazil, Argentina, India Mexico, South Africa, Russia | Dagenham 'H' Building |
| 0142V, 0142X | Taiwan, China |  |
| 0145B, 0145C | Brazil, Argentina | Transfesa |
| 0145H, 0145J | Russia, South Africa |  |
| AP16A, AP24A | USA, Mexico | Coughlin |

NOTE:  This  revision  supersedes  all  previous  versions  of  the  Ford  Packaging Guidelines and Export Packaging Guidelines.     Use these specifications for all parts that do not yet conform to this Ford packaging standard, and for all new business.

EXISTING CONFIRMED PACKAGING DOES NOT HAVE TO BE RE-ENGINEERED

1.3 Supplier Responsibility

All business must be quoted in compliance with these guidelines, and include a breakdown of packaging costs agreed by Ford Purchasing (including any container hire charges and durable/expendable dunnage costs where applicable).

The supplier is responsible for product quality from the manufacturing source to the point of use (linefeed at the assembly line).

All packaging must be developed in accordance with these guidelines, applicable regulatory requirements, QS9000 Quality Systems and Purchase Order Terms and Conditions.

Working  in  conjunction  with  MH&PE  and  the  customer  plant,  the  supplier  is responsible for the design, development and procurement (where appropriate) of their own packaging, and establishing approval from the customer plant.  For special containers, specific approval is also required from Ford MH&PE

Packaging  design  must  protect  the  product,  be  ergonomic  for  users,  and  meet lowest total cost requirements.

All packaging containing hazardous material must have the appropriate regulatory labelling.

Once a packaging specification has been confirmed, the supplier must continue to use this pack, unless otherwise directed by Ford MH&PE or the receiving plant

To  change  a  confirmed  packing  specification,  the  supplier  must  submit  a  new EU1121 Packaging Data Form for approval, one month in advance of the proposed change, to the Ford Packaging Engineer at the receiving plant.

As part of the Ford Policy of continuous improvement, alterations to the approved pack may be requested by the receiving plants.  Suppliers are required to respond quickly to these requests, and manage the packaging change.

In all correspondence with Packaging Engineering, ensure that full contact details are provided, including contact name, Ford Vendor Code (5 digit GSDB Code), e-mail address, and telephone and fax numbers.

1.4 Ford's Environmental Commitment

Ford  is  committed  to  protecting  the  environment  at  every  stage  of  the  production process including transportation of parts to the assembly plants. For this reason packaging must be designed with respect to the following objectives:

Use durable packaging for all Ford European domestic plants

Use of IMC cartons for Export Markets

Use a minimum of internal expendable packaging

Use expendable materials which can be recycled

All plastics (expendable & durable) must be marked with the material identification symbol to aid recycling (see Appendix 5)

1.5  Lean Manufacturing

Ford Motor Company's objective is to be a World Class Automotive Lean Manufacturer. A key enabler of the lean manufacturing process is the packaging for production part shipments from its suppliers. Through the use of optimum sized containers, material flow through the system and line-side ergonomics are improved. The overall effect for packaging is a shift from large packs containing many hours stock, to Small Lot Packaging (i.e. use of smaller containers), containing a target of one hours stock per container.

Why Small Lot Packaging?

When  combined  with  the  Synchronous  Material  Flow  (SMF)  program,  Small  Lot

Packaging generates the following benefits within the production cycle:

Eliminates waste at all stages of the production cycle

Supports the European greening strategy by eliminating cardboard packaging

Reduces freight requirements for European and Export markets by maximising cube utilisation.

Manual delivery replaces mechanical delivery to line-side. Fork lift movements can be replaced by dedicated replenishment cycles

Reduction  in  physical  space  requirements.  Line-side  stock  location,  and  market place storage areas can be significantly reduced

Improves direct labour efficiency. The containers can be ergonomically presented to the operator to maximize their efficiency

Increases inventory turn-over rates Reduces non-value added inventory Smoothes production flow

Reduces	batch	sizes.	Modular	small	lot	packaging	can	be	ordered	and manufactured in smaller units whilst maintaining level load units

With the necessary focus on material flow processes, all these efficiencies can be realized by both Ford and the supplier. Overall, there is no on-cost for operating small- lot packaging.

The Ford Packaging Guidelines have now been up-dated to reflect this on-going Ford commitment to greening and lean manufacture, and emphasize the use of small lot durable containers for European manufacturing plants, and small lot IMC cartons for export manufacturing locations

1.6  Packaging Approval Process

All  packaging  must  be  confirmed  as  acceptable  by  the  user  plant  before  being implemented, normally through timely submission of a EU1121 form.

However, durable packaging and unique containers will involve buy-off of production level prototypes at the plant location before final approval, and this must be included in your timing.   For current model approvals, contact the user plant Packaging Engineer or Export Packaging contact.  For  new model programs, contact the MP&L MH&P Engineer contact, who will monitor and gain plant approvals.

For  any  part,  you  may  be  asked  to  send  a  trial  production  level  pack  before confirmation is given.    You may also elect to send a trial production level pack before finalising your packaging details – contact the appropriate Packaging Engineer.  For Export Packaging, provisional acceptance will be given for compliance with these guidelines, and final acceptance after successful audit by the receiving location.

Remember that you, as the supplier, are responsible for the quality of your product to the point of fit.

1.7  Database Update Process

Packaging data drives a number of processes, including logistics planning (trucks, warehousing, ISO container loading) and scheduling, industrial vehicle and labour requirements, in addition to market place and production layouts.   It is essential that timely and accurate data be provided to support the central database (CMMS3), which feeds many other areas, and that completed EU1121 forms be provided where appropriate.

1.7.1     New Model Programs

For new model programs, packaging data is required 12 months before Job 1, to support the planning and development of the activities mentioned above. To support this, you are required to provide best estimate packaging data as soon as a part is released to you. This will be reviewed by the plant and accepted in principle.

Minimum data required is as follows:

Supplier code (Ford 5 digit GSDB code) Part number and description

Container type, and estimated number of parts in the container. Piece weight of the component

If available, projected daily volume.

The packaging data will then remain firm, unless an engineering change demands a change in specification, or the supplier and/or user plant require a change.

Your MH& P Engineer will get the required approvals from the plant and arrange for the necessary CMMS3 update.  Any further developments, trial shipments, buy-offs, and EU1121 provision, must then take place before the 1PP part of the program.

1.7.2     Current Model Packaging Changes

Changes to current model packaging, or the introduction of new parts to current models, must be done in line with the appropriate VO (see Section 2.3) or Export Packaging (see Section 3.3) selection process, and involve the plant Packaging Engineer or Export Packaging contact. When the EU1121 has been confirmed together with an implementation date, the plant Packaging Engineer will input the revised data to CMMS3.

1.8  Approved Packaging Conformance Process

Following these guidelines means that no parts will be shipped without a confirmed EU1121 specifying the packaging. It is a mandatory requirement for the Supplier to continue to supply in accordance with the confirmed EU1121 and the requirements of these guidelines. The receiving plant will monitor packaging received to ensure conformance with the information logged in the central database (CMMS3). Non- conformance  will  result  in  automatic  rejection  and  Purchase  involvement,  and  may result in the  supplier being  de-merited, and charged for any subsequent re-packing (see Appendix 3 - form EU2714)

IMPORTANT NOTE FOR VO DOMESTIC SHIPMENTS:   Whilst Ford expects all suppliers to ship parts in the approved durable container, emergency expendable packaging is sometimes unavoidable.   If this situation occurs the receiving plants must be informed prior to shipment, and packs must be identified as emergency packaging (see section 2.10, Emergency Expendable Packaging User Guide). Failure to do so will result in automatic part rejection.

In order  to  support  the  lean  manufacturing  system,  it  is  important  for  suppliers  to develop  emergency  expendable  packaging,  which  replicates  the  durable  solution  in size, pack density and stack height during transport.   A minimum of 3 days stock of emergency expendable packaging should be available to meet any such contingency.

If costs are to be claimed against Ford or the third party container provider, details of the reasons and associated costs for using emergency expendable packaging must be kept.     If  the  third  party  container  provider  fails  to  deliver  the  required  durable containers, details of the specific container orders and the failed deliveries (including dates and quantities) must be provided in support of any claims for costs against the provider.

1.9 Continuous Improvement

Ford operate a policy of continuous improvement, and requests to change confirmed packaging may be sought by the supplier, or Ford, in pursuit of this.   Suppliers are asked  to  respond  quickly  to  any  requests  for  change,  and  re-submit an amended EU1121 for confirmation and CMMS3 update, at least one week prior to the implementation date of the revised packaging.

1.10	Final Checklist

To ensure that you have used these Packaging Guidelines correctly please use the following checklist to tick off that all key steps have been taken:

1.	You  have  selected  an  approved  standard  container  or  an  agreed durable alternative for European Shipments, or an approved IMC carton for  Export  Shipments,  using  the guidelines, flowcharts and    tables in these Guidelines.

2.	You have sent an EU1121 (European/Export Shipments – Appendix 2)

to the Ford Packaging Engineering contact.

3.	You  have  received  'Confirmed'  approval  for  European  shipments,  or

'Provisional Approval' (Export Shipments) for the proposal(s).

4.	You have selected the appropriate labels, and for Export Shipments the correct pallet base, weight disc, stickers and handles to be used when shipping this packaging.

5.	For Export Packaging, you have selected a packaging supplier that can provide the approved carton to the performance specification detailed in Section 2.2

6.	You have selected appropriate supplier(s) that can provide each of the above and can support your shipping volumes and program dates.

7.	You  have  provided  appropriate  training  for  staff  to  ensure  that  user, consolidation and shipping guidelines are complied with.

8.	You  have  the  appropriate  documentation  and  internal  processes  to ensure that container ordering and tracking both inbound and outbound are	robust,   and  shipments   are   always   shipped   to   the   approved specification.

PART 2

EUROPEAN MANUFACTURING PLANTS

Applies to all European suppliers supplying components to Ford manufacturing locations in Europe.

Use Durable Packaging for shipments to the following plants:

| 0134A 0096A | Cologne Genk | Body and Assembly Operations Body and Assembly Operations |
| --- | --- | --- |
| 0097A 0145A | Saarlouis Valencia | Body and Assembly Operations Body and Assembly Operations |
| 0118A | Southampton | Body and Assembly Operations |
| 0116A 0119A | Croydon Dagenham | Stamping Operations Stamping Operations |

NOTE: This revision supersedes all previous versions of the Ford VO European Packaging Guidelines.  Use these specifications for all parts that do not yet conform to this Ford packaging standard, and for all new business.

EXISTING CONFIRMED PACKAGING DOES NOT HAVE TO BE RE-ENGINEERED

|  | Part 2 Contents | Page |
| --- | --- | --- |
| 2.1 | Introduction to European Durable Containers………………..………. | 12 |
| 2.2 | Standard Containers Details………………………………………………. | 12 |
| 2.3 | Container Selection Process……………………………………………… | 15 |
|  | 2.3.1 Selecting the Container – Trim and Assembly Plants………… | 15 |
|  | 2.3.2 Container Selection Flowchart…………………………..…….… | 16 |
|  | 2.3.3 Selecting the Container – Metal Stamping and Body Plants… | 17 |
|  | 2.3.4 Packaging Costs…………………………………………..……… | 17 |
| 2.4 | Container Control ..………………….............……………………………... | 18 |
|  | 2.4.1 Ford Owned Container Control…………..……….…………….. | 18 |
|  | 2.4.2 Third Party Owned Container Control………………………….. | 18 |
|  | 2.4.3 Supplier Owned Container Control ……………..……………… | 19 |
| 2.5 | KLT User Guide…………………………………………………..………….. | 20 |
|  | 2.5.1 KLT Labelling Requirements….…………………………………. | 20 |
|  | 2.5.2 KLT Unit Load Construction……………………………………... | 22 |
|  | 2.5.3 KLT Unit Load Rules……..….…………………………………… | 23 |

| 2.6 | FLC / FSC User Guide (Trim and Assembly Plants Only)….…....……. | 24 |
| --- | --- | --- |
|  | 2.6.1 FLC/FSC Labeling Requirements…………….…….…..………… | 24 |
|  | 2.6.2 FLC/FSC Operating Rules….……………..……………..………… | 25 |
| 2.7 | FORD ODETTE/UZE Container User Guide.………………..….………… | 26 |
|  | 2.7.1 ODETTE Container Rules……………….…………………………. | 26 |
| 2.8 | Special Container User Guide..………………..………..………………….. | 27 |
| 2.9 | Internal Packaging Requirements…………………………..……………... | 28 |

2.9.1 Internal Packaging Rules…………………………………………….	28

2.10 Emergency Expendable Packaging User Guide….…….....……….….. 29

2.10.1 Emergency Expendable Material Selection ………………………  30

2.1 Introduction to European Durable Containers

Durable packaging solutions are required for all shipments to the above plants and standard containers are preferred. Optimal are the small manually handled KLT containers. If your part is too large for these, the FSC/FLC container should be

selected for shipments to PTA plants, or Ford owned Odette/UZE5/ZE39 containers for

shipments to MS&B plants. If these are also unsuitable, a unique durable container is required, and you must contact Ford Purchasing and MP&L MH&PE before proceeding further.

Ford steel containers are available through the  receiving  MS&B  plants,  and  plastic containers through third party container providers, viz.:

Volvo Emballage	for FLC/FSC containers (from June 2002).

Chep Automotive	for KLT containers (and FLC/FSC until June 2002)

Before a supplier can order containers through the third party provider, he must have signed a standard agreement (this agreement is pre-arranged with Ford and applies to all suppliers). The supplier is then entitled to order containers within the limits of his allocation.

It is the suppliers' responsibility to ensure that this agreement is in place on a timely basis.

The  durable  Ford  standard  containers  specified  below  must  be  used  wherever possible.  If they are not suitable for your product, 100% returnable packaging funded by the supplier must be used (authorisation and specification to be agreed individually with Ford Packaging Engineering and Ford Purchasing).  Follow the container selection process in Section 2.3.

2.2	Standard Container Details

Third Party Containers

(Note: Container details are for guidance – precise details can be obtained from the container provider)

KLT 3214 	KLT4314

External cms: 30 x 20 x 14	External cms: 40 x 30 x 14

Internal cms : 27.1 x 13.6 x 13	Internal cms : 33.4 x 24.7 x 10.4

Tare weight: 0.7 kg	Tare weight: 1.6 kg Net capacity: 11.3 kg	Net capacity: 10.4 kg Max gross weight: 12 kg	Max gross weight: 12 kg

KLT 4328 	KLT 6428

External cms: 40 x 30 x 28	External cms: 60 x 40 x 28

Internal cms: 33.4 x 24.7 x 23.6	Internal cms: 53.2 x 34.6 x 23.1

Tare weight: 2.6 kg	Tare weight: 4.4 kg

Net capacity: 9.4 kg	Net capacity: 7.6 kg

Max gross weight: 12 kg	Max gross weight: 12 kg

Trim and Assembly Containers

FSC 1206 	FLC1210

| External cms: 120 x 100 x 59.5 | External cms: 120 x 100 x 97.5 |  |
| --- | --- | --- |
| Internal cms: 111.5 x 91.5 x 38.2 | Internal cms: 111.5 x 91.5 | x 75.7 |

Folded height: 41 cms	Folded height: 41 cms

Tare weight: 43 kg	Tare weight: 63 kg

Net capacity for internal Ford use:	Net capacity for internal Ford use:

* 270 kg for non-fork truck handling	* 250 kg for non-fork truck handling

*  500 kg for fork truck handling	* 500 kg for fork truck handling

Max gross weight: 543 kg	Max gross weight: 563 kg

MS&B Containers

UZE 038/039 	UZE 05

| UZE 039 External: 220 x 120 x 101 | UZE 038 External: 120 x 100 x 101 | UZE 05 External: 120 x 100 x 76 |
| --- | --- | --- |
| Internal : 206.5 x 113.0 x 70.5 | Internal: 113 x 83.5 x 70.5 | Internal: 115 x 95 x 66 |
| Tare weight: 241 kg Net Capacity: 2000 kg Max gross weight: 2241 kg | Tare weight: 180 kg Net Capacity: 2000 kg Max gross weight: 2180 kg | Tare weight: 160 kg Net capacity: 3000 kg Max gross weight: 3160 kg |

(All dimensions are in centimeters)

Odette 8401/8402 	Odette 8421/8422

Odette 8401:	Odette 8421:

External cms: 120 x 100 x 75 	External cms:  120 x 100 x 75

Internal cms: 113 x 93 x 55.6 	Internal cms:  113 x 93 x 55.6

Folded Height: 30 	Folded Height:  30

Tare weight:  127 kg 	Tare weight: 117 kg

Net capacity:  1000 kg 	Net capacity:  1000 kg

Max gross weight: 1127 kg 	Max gross weight: 1117 kg

Odette 8402:	Odette 8422:

External cms: 120 x 100 x 100 	External cms: 120 x 100 x 100

Internal cms: 113 x 93 x 80.6 	Internal cms :  113 x 93 x 806

Folded height: 40cms 	Folded Height: 40 cms Tare weight:  138 kg 	Tare weight:  137 kg Net capacity:  1000 kg 	Net capacity: 1000 kg

Max gross weight: 1147 kg 	Max gross weight: 1137 kg

2.3 Container Selection Process

Now that small lot packaging is firmly established the container selection process has been simplified  to reflect current requirements.    The flow chart opposite  (see 2.3.2) will ensure that your container selection meets European production requirements.

2.3.1 Selecting the Container – Trim and Assembly Plants

Container selection must be made on the basis that the smallest container is used to meet

Ford requirements.

1.  Establish  how many shifts the destination  plant is working  for the plant(s)  you are supplying – multiply by 7.1 hours to give the hours worked per day.

2.  Next,  take  your  projected  daily  delivery  and  divide  by  the  hours  worked  per  day

(from (1) above).   This is the optimum container quantity and gives 1 hour of stock for your component.

3.  From the standard container range, select the smallest container that will hold this 1

hours  worth  of  stock.     Now  fill  the  container.     This  is  the  optimum  container specification.

4.  Is the gross weight of the container within the allowed maximum:

a).  12 kg for KLT containers?

b). 313kg for FLC/FSC for fork truck free handling OR

c). 563kg for FLC/FSC for fork truck handling

If  YES,  this  is  your  container  specification.  If  NO,  contact  your  Ford  Packaging

Engineer.

5.  Determine if any internal packaging is required to ensure quality.

6.  Complete  the  EU1121  form,  including  details  of  any  internal  dunnage  used,  and submit  to  Ford  Packaging  Engineering  (include  photograph  of  all  FLC/FSC  and unique containers, and any KLT container with internal dunnage).

7.  Once confirmed (see 1.4 below), use only this specification to ship into Ford.

Exceptions

If the component  will not fit a standard  container  according  to the above  process, contact your Ford Packaging Engineer.

Hardware  (fasteners  etc)  and  small  parts  should  automatically  be  specified  in  a

KLT3214 container and filled (not exceeding the 12kg limit).

If  a  part  is  already  supplied  to  another  plant  in  Ford  approved  packaging  which meets these guidelines.

If  a  new  part  is  to  be  shipped  to  more  than  one  plant,  use  the  packaging specification for the user with the highest daily volume.

FSC  containers  should  only be specified where use of an FLC would compromise quality or exceed the weight limit.

If  durable  dunnage  or  unique  containers  (FORD  or  SUPPLIER  OWNED)  are specified,  contact  Packaging  Engineering  before  proceeding.    These  items  will  be subject to a full cost analysis, including the return freight costs.    If agreed, method of  payment  must  be  authorised   by  Purchase,  before  any  commitments   are made.  Design must proceed in conjunction with Packaging Engineering to ensure ergonomic and process requirements are met.

Durable  dunnage  must  be  designed,  developed,  and  operated  in  accordance  with the Durable Insert and Stretch Container Standard  - see  Appendix 6

2.3.2. Container Selection Flowchart

Example:

Select part	Part XYZ weighs 0.032kg and is

in question	to be delivered to a 2 shift plant at a rate of 2800/day

Does it fit a	No standard container?

Part will fit a standard

Yes	container

Yes		Is it a fastener? (screw, clip, plug etc)

No

Part is not a fastener

Determine number of shifts	Example:

worked and multiply by 7.1	2 shift operation

= hours worked per day	= 2 x 7.1hrs

= 14.2 hours/day

Take projected daily	Example:

delivery quantity and	Projected DPV = 2800

divide by hours worked per day	2800 / 14.2 = 197 parts

= optimum container quantity	Optimum quantity = 197

Select the smallest standard	Example:

container to hold this quantity:	Smallest container to

Select KLT3214	Trim and Assy = KLT/FLC/FSC	hold 197 parts is KLT6428

MS&B = KLT/Odette/ZE range	To fill container takes 230 parts

- now fill the container

Is containe	No within specified

weight range?	Example:

KLT6428 tare weight = 4.4kg

Yes	230 Parts x 0.032kg = 7.36kg

Total weight = 7.36kg + 4.4kg = 11.76kg

Advise the Packaging Engineering contact, obtain approvals,

and provide packaging

Example:

Contact Ford Packaging

Engineer and/or Purchase

specification/documentation

Container specification is: KLT6428 with 230 parts and gross weight of 11.76kg

2.3.3 Selecting the Container – Metal Stamping and Body Parts

The Ford policy of 100% durable packaging applies equally to European MS&B plants, but the different nature of the products is reflected in the different containers available. The container range is as follows:

KLT containers - to be used for small parts and hardware. Selection process is the same as Trim and Assembly (see section 2.3), with a maximum gross weight of 12kg.

Odette containers – to be used for all other medium sized parts that can be loaded to the container

ZE 39 containers – to be used for parts too large to fit into an Odette container. UZE 5 containers – for heavy parts, or small parts unsuitable for meshed containers.

Unique containers – used for skin surface parts.  Unique containers will involve additional investment for design/development/procurement. Suppliers must not proceed with unique containers before consulting MH&PE and Ford Purchase, to clarify funding arrangements and technical requirements.

2.3.4 Packaging Costs

Packaging costs must be identified and integrated as part of your piece price at the quotation stage, and can only be agreed by Ford Purchase (your commodity buyer).  Confirmation of an EU1121 advises that your packaging proposals are

acceptable to the user plant, and does not infer or imply acceptance or agreement

of any associated costs with that packaging.

2.4  Container Control

Suppliers are responsible for ensuring the ordering, control, and documentation procedures appropriate to the type of container they are using.  Failure to do so may result in emergency packaging and transport being used, and any costs for this will be the sole responsibility of the supplier.

There are three types of container control potentially required:

a). Ford Owned Containers (see 2.4.1)

b). Third Party Owned Containers (see 2.4.2)

c). Supplier Owned Containers (see 2.4.3)

2.4.1 Ford Owned Containers

These  include  the  steel  Odette/UZE5/ZE39  containers,  and  special  racks. Arrangements for the supply and control of these containers must be made through your MPL contact of the receiving plant.    Details may vary according to the local conditions and specific requirements for each container.

2.4.2 Third Party Container Management

For Paint, Trim and Assembly standard containers, Vehicle Operations employ a container strategy with containers owned and managed by Ford approved third party container management companies. Containers are shipped from the European supply base to the following assembly and body construction locations:

Southampton, Saarlouis, Valencia, Genk, Cologne, Croydon, Dagenham

When  empty,  the  containers  are  consolidated,  and  returned  via  the  most  efficient routing  (i.e.  not  necessarily  their  customer  plants).    (NB!  Containers  must  not  be shipped to any location, other than those listed above.   Containers shipped to other destinations will remain on the supplier account and be deemed lost.  Lost containers fees will be levied by the 3rd party provider, in line with the standard agreement).

A standard agreement must be signed before containers can be issued, and the allocated account manager will then provide details on specific container ordering and shipping procedures.

For FLC and FSC containers, a container allocation is calculated, providing the supplier with a maximum 5 day float.  The allocation is based on projected volumes of parts to be shipped to the various plants, and is reviewed periodically.  Containers are only provided to support shipment from the last manufacturing operation in the contracted supplier plant, to point of use in Ford.  Containers are not provided for supplier intra plant movements, in-process handling, stockpiling or emergency needs, which remain the responsibility of the supplier.

It is the supplier's responsibility to ensure that container ordering, control, and documentation procedures are fully complied with, including records of containers and dates  when  ordered,  and  any  failed  deliveries.       The  supplier  must  also  ensure container returns are fully documented  and advised on time, and that the approved allocation of containers is not exceeded.

Failure to comply with any of the above may result in the 3rd  party container provider assuming the supplier has received the allocated container requirement, and further containers  will  then  be  denied.     The  cost  of  any  emergency  packaging  and transportation measures resulting from such a situation will be the sole responsibility of the supplier.

From June 2002  the Internet can be used to order FLC/FSC containers, and monitor their delivery status and the account balance.  Suppliers will be expected to use these facilities to ensure the use of emergency expendable packaging is minimised (further details will be issued prior to launch).

2.4.3 Supplier Owned Containers

These can include any type of standard or special racks, but must not be used without completing  the  Container  Selection  Process  (see  Section  2.3)  and  gaining  the necessary approvals.   Particular attention must be paid to the identification of supplier owned containers, to aid recognition and indicate return delivery location in the event of a mis-directed shipment.   Unique numbers are issued by Ford MH&PE for each insert or special container type e.g. FE10946 or FLCDU6.    These numbers not only aid identification, but are entered into the Ford CMMS3 system for container control.

Arrangements for control and routing of these containers must be made through your MP&L contact at the receiving plant.    Details may vary according to local conditions and the specific requirements for each container.

If the packaging concerned is a durable insert used in conjunction with a standard container, or a stretch container, ensure that the Durable Insert and Stretch Container Standard (see Appendix 6) is complied with, including completion of the specifications and Tracking Sheet, to identify the routing and responsibilities of the return process.

It  is  recommended  that  this  process  is  adopted  for  returns  of  all  supplier  owned containers to identify routing and responsibilities, before shipments are commenced.

2.5  KLT User Guide

The KLT container system comprises a range of four modular box sizes combined with two pallet sizes and lids (see section 2.2.1).  The KLT ordering and control system is administered through the 3rd  party provider (Chep Automotive), details of which are available through your account manager.  All KLT containers are limited to a maximum gross weight of 12kg (i.e. including the weight of the container and any dunnage used)

– there are no exceptions to this requirement.

Unit load of 30 brick-built KLT4328 containers. Containers are assembled using an approved 3rd Party pallet base and cover. Plastic banding (2 off) has been applied without limiting access to four-way

pallet base.

KLT's should always be shipped in unit load format with one or more complete layers of KLT containers up to a maximum of 1.00 metre high. Unit loads may comprise one part number, or multi- part numbers in a mixed load.

Note:  Some parts have a very low daily call-in and it is difficult to make up a single layer of containers for inbound shipment.   Under these circumstances, contact the Plant Supply Chain Management analyst responsible for the part concerned, and agree upon one of the following options:

Review feasibility of mixed load shipments from supplier to plant.

Request Release and Follow Up to adjust call-in frequency to allow a minimum of one layer of KLT containers to be shipped (at more extended periods).

2.5.1 KLT Labelling Requirements

Container labels are based on the current Odette standard, printed on white weather resistant paper of weight 160-170g/m2  with black text. These printed labels must be to latest MP&L requirements, and must include ILVS (In-Line Vehicle Sequencing) and

'Control Item' marking where appropriate. Please refer to the  MP&L contact person shown in Appendix 1 for further information.

Use a minimum of (1) Odette standard label, coloured white, per KLT container

Locate  "A5"  sized  Odette  label  in  label  holder,  ensuring  label  is  of  sufficient thickness to remain securely located in holder - (if necessary, a small sticker may be required to secure a label. This must be a "low adhesion" sticker, one sticker per label, with majority of sticker on label and not KLT)

Ensure that label is positioned outwards within the unit load wherever possible

For KLT3214 containers fold the label top and bottom to reduce label size to fit label  holder  –  ensure  that  part  number,  quantity  and  supplier  code  are  clearly visible.

If a single part number is being shipped;

Use (2) master labels, coloured green. The master labels should be attached to adjacent sides of the unit load, attaching across lid and KLT using "low adhesion" stickers. Master labels must show part number, and total quantity of parts.

Unit Load of KLT 6428 containers showing correct positioning of either MIXED LOAD or MASTER label.

If multiple part numbers are being shipped within a unit load:

Use (2) mixed load labels, coloured green. The mixed load labels should be attached to adjacent sides of the unit load, attaching across lid and KLT using "low adhesion"  stickers.  Mixed  load  label  must  show  all  part  numbers,  with  total quantities of all parts shipped.

DO NOT use self adhesive Odette labels under any circumstances

KLT 3214 Container with A5

Odette label in label holder

--affix using single "low adhesion" sticker

21

2.5.2 Construction Guidelines

The Unit Load is designed to maximise Freight, Logistics and In-Plant Handling efficiencies. When constructing the Unit load, follow the guides listed below:

1.

Ship with  Complete Unit load of full KLT containers

a) One part number	b) Mixed part numbers

Example:

98AB 12K531 BC

XS41 7A512

If a complete unit load is not possible…..

2.

Ship with Complete Layer(s) of full KLT containers.

a) One part number	b)  Mixed part numbers

Example:

98AB 12K531 BC XS41 7A512 DD

NOTE

The  modular  nature  of  KLT  containers  means complete layers of 4314's, 4328's or 6428's can be shipped within the same unit load. Complete layers of

3214's can also be included within a larger load unit, provided they form the base layer(s)

2.5.3 KLT Unit Load Construction

The following rules apply to all KLT unit loads:

DO ensure that all containers are clean, serviceable and free from redundant labels, prior to loading components

DO report complaints to your 3rd Party contact if received containers are in an unacceptable condition

DO assemble KLT unit loads using only the specified 3 rd Party pallet base and cover

*KLT 4314, 4328 and 6428 can only be assembled on 100 x 120 pallet

*KLT 3214 can be supplied on either 100 x 120 pallet or 100 x 60 pallet

DO ensure that 6428, 4328 and 4314 container unit loads are "brick built" as shown.

DO position KLT containers on pallet base with product labels facing outwards

DO use two plastic bands to secure the KLT unit load to the pallet base

DO  NOT ship "pyramid loads" under any circumstances

DO  NOT exceed a unit load height greater than 100 cm

DO  NOT mix loads of cardboard boxes and KLT containers

DO  NOT ship empty KLT containers to make up complete layers

DO  NOT exceed 12kg gross weight of each container

DO  NOT compromise access to pallet base with banding straps

DO  NOT use steel banding as it is difficult to remove and can cause injury

DO  NOT use shrink or stretch wrap

2.6 FLC/FSC User Guide (Trim & Assembly Plants only)

The FLC 1210 (Folding Large Container) is a unit load sized (120 x 100 x 97.5 cm) container with drop-down access doors on two adjacent sides. The FSC (Folding Small Container) shares a common base, with a reduced overall height (120 x 100 x 59.5 cm), and no access doors.  Both containers are intended for 'clean' parts only (i.e. Trim and Assembly parts), and fold to improve cube utilisation for the return journey. FSC containers are only used where use of an FLC would compromise quality or exceed the weight limit. In addition to the containers, there is a separate non-load bearing dust cover, which can be fitted to both containers (not normally used with FSC containers).

2.6.1 FLC / FSC Container Labeling Requirements

Container labels are based on the current Odette standard, printed on white weather resistant paper of weight 160-170g/m2 with black text. These printed labels must be to latest MP&L requirements, and must include the dock code and marketplace address, in addition to ILVS (In-Line Vehicle Sequencing) and 'Control Item' marking where appropriate. Please refer to the appropriate plant MP&L contact person for further information.

Use a minimum of two "A5" Odette labels, on adjacent sides of the container

L ocate labels in the label holders provide.

DO NOT use self adhesive Odette labels

Affix label using low adhesion sticker, if required

2.6.2  FLC / FSC Operating Rules

Sketch showing correct positioning for labels applied to adjacent sides of an FLC container

DO ensure that all containers are clean, serviceable and free from redundant labels, prior to loading

DO 	report complaints to your 3rd   Party contact if received containers are in an unacceptable condition.

DO ensure the lugs clip into dedicated location points in the container when fitting the dust cover to the containers

DO  fold containers sides in the correct sequence if required (refer to 3rd   Party

Container Supplier operating guide)

DO develop and ensure 3 shipments worth of an emergency expendable pack is always available. This must mirror the FLC / FSC in size, pack density and stackability. Refer to guidelines in section 2.10.

DO only ship to approved locations

DO stay within your 5 days container allocation

DO NOT floor stack erected containers more than 5 high

DO NOT use any form of banding on the container (unless expressly required to by

Ford Packaging Engineering)

DO NOT store obsolete stock in Ford containers

DO NOT use durable containers for export destinations

DO NOT exceed the gross weight capacity of the container:

FLC/FSC	313Kg gross weight for fork truck free handling (normal)

FLC/FSC	563Kg gross weight for (confirmed) fork truck handling

2.7 Ford ODETTE / ZE38/39 / UZE5 Container User Guide

(MS&B Plant Only)

KLTs must be used wherever possible within the 12kg maximum weight limit.  However, when this is not feasible for your product, select:

1.  Odette container for normal parts

2.  ZE38/39 for parts too heavy or large for an Odette container

3.  UZE5 for very heavy small/medium parts

4.  Special containers for major skin panels and/or quality sensitive parts

2.7.2  Ford ODETTE / ZE38/39 / UZE5 Operating Rules

DO ensure that all containers are clean, serviceable and free from redundant labels, prior to loading

DO ensure that the pallet is properly labeled  – for Odette containers follow the

FLC/FSC labeling procedure (see section 2.6.1).

DO report complaints to your supplying plant contact if received containers are in an unacceptable condition.

DO ensure containers are securely erected before loading.

DO fold containers sides in the correct sequence as required

DO ensure container control is operated for Odette/UZE5/ZE39 containers, (see

Section 2.4 Container Control).

DO develop and ensure 3 shipments worth of an emergency expendable pack is always available. This must mirror the Odette Container in size, pack density and stackability (see section 2.10).

DO NOT floor stack erected containers more than 6 high

DO NOT exceed the net capacity of the container:

ODETTE	1000kg NET weight for fork truck handling UZE 039/038	2000kg NET weight for fork truck handling UZE 05	3000kg Net weight for fork truck handling

2.8	Special Container User Guide

Where special packaging is required please contact MH&PE to discuss the specific requirements.

All special packaging economics (including, where relevant, any container hire charges and durable or expendable internal dunnage costs as applicable)must be reviewed and agreed by Ford Purchase and Packaging Engineering.

All  special  packaging  must  be  formally  approved  by  the  appropriate  Ford  customer location(s) in conjunction with your Ford MH&PE contact.

It is Ford Motor Company’s long term objective, to adopt 100% supplier ownership for all special packaging. It will be a supplier's responsibility to design, develop and procure special packaging. This on-going process will be implemented on an individual basis in close conjunction with Ford Purchase and MH&PE.

The supplier must also ensure that all special packaging is clean, serviceable and free from redundant labels, prior to packing components. Damaged and/or dirty containers will not be accepted by your customer.

It  is  the  Supplier’s  responsibility  to  repair  and  maintain  special  packaging.  All  special packaging fleets to be determined in conjunction with Ford MH&PE.

Ford MH&PE will advise on quality assured packaging development service providers. For special containers, Container Control (see Section 2.4) is still applicable

Example of special rack with unique internal fittings designed for a specific part.

Odette type labels positioned on adjacent corners in label holders provided.

Example of extended KLT container with special durable inserts

Example of ext ended FSC container with unique identification on base

2.9  Internal Packaging

In line with Ford's greening policy, internal packaging should be kept to an absolute minimum, consistent with ensuring product quality to the point of use, and product function during the product life-cycle.

Where use of expendable packaging becomes a significant operating cost/piece price element, durable inserts or packaging should be evaluated in conjunction with Ford Packaging Engineers.

All expendable packaging must be re-cyclable and all plastics (expendable & durable) must be marked with the appropriate material identification symbol to aid recycling (see Appendix 5)

2.9.1 Internal Packaging Rules

DO ensure that part quality is maintained using the minimum of internal packaging

DO ensure that it is not possible for parts to tangle during transportation (consider banding/bundling parts together to minimise the risk).

DO ensure that all expendable dunnage is re-cyclable (see section 2.10.2)

DO pack containers to utilize at least 95% of internal volume

DO ensure that expendable dunnage can be easily removed from the container

DO ensure that your internal dunnage costs are included in ESTA quotes

DO NOT use shrink or stretch wrapping materials for VO European shipments

DO  NOT wrap parts in plastic bags (consider using inter-woven foam layer pads).  Use of plastic bags requires specific written agreement from MH&PE or the user plant MP&L contact.

DO NOT mix different part numbers within the same container, unless requested in writing by the user plant MP&L contact.

2.10  Emergency Expendable Packaging User Guide

Expendable packaging is only to be used for emergency shipments when the durable containers are not available due to unforeseen circumstances.

It is essential that an emergency expendable packaging solution is developed and 3 shipments worth  are  always  available  at  the  supplier  location.  THE  EMERGENCY   EXPENDAB LE PACKAGING MUST  EXACTLY REPLICATE THE DURABLE SOLUTION IN SIZE, PACK DENSITY  AND  STACKABILITY,  and  be agreed  by the  receiving  plant  SMF  team.  This  is absolutely  mandatory  since the part ordering  and external  and internal logistics  systems  are based specifically on the container size and part quantity.

Under no circumstances should emergency expendable packaging be used to ship production material to markets outside Europe (see Part3 Export Operations).

ACCEPTABLE

Able to safely stack in storage and transit to same height as durable equivalent

Max. height

100 cm 	Full Perimeter pallet

UNACCEPTABLE

NOT ACCEPTABLE

Collapsed stack

1.Two way entry

2. Fibre pallet

3. OK for Europe Use full perimeter base for exports

No banding

Pyramid load

Banding under pallet base

(restricts fork

2.10.1  Emergency Expendable Material Rules

DO develop and ensure 3 shipments worth of emergency expendable packaging is always available.

DO  only use expendable external packaging in an emergency when no durable containers are available and after concurrence by the receiving plant

DO make all packaging into unit loads ( for fork lift handling of packaging units)

DO make unit loads flat topped. Incomplete layers (pyramid loads) are not allowed under any circumstances.

DO label all emergency expendable packaging clearly, stating that the pack is emergency packaging.

DO use banding or strapping made of plastic

DO use pallets made of solid wood with four way entry.

DO always use full perimeter expendable pallets (see drawing on previous page)

DO NOT use steel banding as it is difficult to remove and can cause injury.

DO NOT use shrink wrap or stretch wrap without written permission from the local

Material Handling Engineer. Ford fire regulations do not permit this practice.

DO  NOT allow cardboard packaging to overhang the pallet, it does not stack properly and is likely to get damaged.

DO NOT use paper board, moulded chip or plastic expendable pallets.

DO NOT staple carton to the base pallet

2.10.2 Emergency Expendable Material Selection Guide

When selecting expendable material for use in emergency packs, or internal dunnage, ensure that all national legislation is adhered to. The Ford preferred materials are:

Timber:

must be untreated, natural solid wood. fibreboard, chipboard etc. are not allowed.

no additional coatings or preservatives are permitted. must not have plastic foil adhered to it.

Paper, cardboard:

must not include additives in the raw paper or board.

materials used for waterproofing, impregnation, gluing etc. must not inhibit re-cycling.

Plastic Sheets and Foils:

use polyethylene, polypropylene or ABS

where printed, the surface area of the ink must not exceed 3% total surface. adhesive tapes and stickers should be polyethylene or polypropylene.

PART 3

Export Operations

Applies to all suppliers shipping exports through the following Ford

Trading Companies:

Use Export Packaging for:

European

Plant Code	Destination	Consolidator

0134D, 0134F, 0134T, 0134H	Brazil, Argentina	P. Huppertz

0134R, 0134U	Mexico, South Africa

0142S, 0142T, 0142W, AYFUA	Turkey, Taiwan, Russia

| 0134E, 0134G, 0134 | Brazil, Argentina, India | Dagenham |
| --- | --- | --- |
| 0134Q, 01420, 0142U | Mexico, South Africa, Russia | 'H' Building |
| 0142V, 0142X, 0142W, AYFUA | Taiwan China |  |

| 0145B, 0145C | Brazil, Argentina | Transfesa |
| --- | --- | --- |
| 0145H, 0145J | Russia, South Africa |  |

AP16A, AP24A                                 USA, Mexico                                     Coughlin

NOTE: This revision supersedes all previous versions of the Ford Export Packaging Guidelines.    Use these specifications for all parts that do not yet conform to this Ford packaging standard, and for all new business.

EXISTING APPROVED EXPORT PACKAGING DOES NOT HAVE TO BE RE-ENGINEERED

Part 3 Contents

3.1	Introduction…………………………….…………………………..

33

Page

3.2	IMC Carton Specifications…………….…………………………

34

3.3	IMC Carton Selection Process……….…….…………………..  35

2.3.1 Packaging Costs………………………………………………………....	35

2.3.2 IMC Selection Flow Chart………………………………………….……	36

3.4	DO'S………………………………………………………….……..	37

3.5	DO NOTS………………………………………….………………..

38

3.6	IMC Carton User Guide………………..………………………..	39

2.6.1 Loading Cartons to Base………………………………………………	39

2.6.2 Loading Cartons to Base by IMC Type…………………………….…	40

3.7	ISO Modular Pallet Dimensions …………………..…………...  41

3.1   Introduction

Export packaging differs from the European domestic production requirements by using IMC (International Modular Cartons) packs instead of durable standard containers.  To support lean production and minimise freight costs for our export locations, the IMC cartons have been developed using the same principles applied in Europe.

Please note that there is no longer any re-pack operation for Trim and Assembly parts, and the IMC cartons are consolidated by the Ford Trading Companies as received, for onward shipment to the final destination.

This section of the Packaging Guide is to advise Ford suppliers of the packaging requirements, and standardise the method of shipment to all export markets.

If you are unsure as to which territories are deemed as export for your company, please contact either your Ford buyer, Supply Chain Management contact or MP&L MH& PE contact.

An EU1121 must be completed for each part/d estination shipped and returned to the appropriate Ford Packaging Engineering department.

Please ensure you communicate your proposals via e-mail - to obtain an electronic version of the EU1121 either contact the appropriate e-mail address below or visit the Global Terms & Conditions Page in the Ford Intranet.

Contact the following for parts exported from:

| EUROPE Metric Units | NORTH AMERICA Imperial Units | INDIA Metric Units | SOUTH AMERICA Metric Units |
| --- | --- | --- | --- |
| Tel: 44 (0) 1708 67 3089 | Tel: (313) 845 -4315 | Tel: 91 4114 54375 x3029 | tbe |
| Fax: 44 (0) 1708 67 2211 Eu1121e@ford.com | Fax: (313) 323 -8279 na1121e@ford.com | Fax: 91 4114 54081 in1121e@ford.com | tbe sa1121e@ford.com |
| FAO: MH&PE FAO Packaging FAO Packaging FAO Packaging Engineering Engineering Engineering IEO (EU1121) Dept. IEO (EU1121) Dept. IEO (EU1121) Dept. IEO (EU1121) Dept. Room 20/220 QMP Building, S P Koil Post tbe Ford Motor Co. Maildrop 619 Chengalpattu - 603 204 Arisdale Avenue. 17101 Rotunda Drive, Tamil Nadu South Ockendon Essex. Dearborn, MI 48121 India RM15 5TJ. UK USA |

[NOTE: EU1121 forms for North American destined material, must have details stated in English Imperial measurements (inches, pounds, lbs), all other destinations are to use Metric measurements (mm, kg)]

3.2 IMC Carton Specifications

ISO-MODULAR CARTON – PERFORMANCE SPECIFICATION

| Carton Number | Exterior Dimensions (mm) L W H | Exterior | Weight (est.) Kg. (lbs) | CARTON SPECIFICATION | Box Type |
| --- | --- | --- | --- | --- | --- |
|  |  | Dimensions (in) |  | Min. Comp. | Burst Strength | Punctur e Resist. |  |
|  |  | L W H |  | (Kg) | (kPa) | (J) |  |
| IMC010# IMC011* | 140 140 | 240 240 | 120 120 | 9.5 9.5 | 5.5 5.5 | 4.75 4.75 | 0.1(0.2) 0.3 (0.7) | 208 208 | 1320 1320 | 6 6 | 201 0422x2* |
| IMC020# | 140 | 240 | 240 | 9.5 | 5.5 | 9.5 | 0.2 (0.4) | 208 | 1320 | 6 | 201 |
| IMC030# | 280 | 240 | 120 | 11 | 9.5 | 4.75 | 0.2 (0.4) | 243 | 1320 | 6 | 201 |
| IMC031* | 280 | 240 | 120 | 11 | 9.5 | 4.75 | 0.4 (0.9) | 243 | 1320 | 6 | 0422x2* |
| IMC040# | 280 | 240 | 240 | 11 | 9.5 | 9.5 | 0.3 (0.7) | 243 | 1320 | 6 | 201 |
| IMC050# | 280 | 480 | 120 | 19 | 11 | 4.75 | 0.4 (0.9) | 294 | 1320 | 6 | 201 |
| IMC060# | 280 | 480 | 240 | 19 | 11 | 9.5 | 0.8 (1.8) | 294 | 1320 | 6 | 201 |
| IMC070# | 560 | 240 | 120 | 22 | 9.5 | 4.75 | 0.4 (0.9) | 301 | 1320 | 6 | 201 |
| IMC080# | 560 | 240 | 240 | 22 | 9.5 | 9.5 | 0.5 (1.1) | 301 | 1320 | 6 | 201 |
| IMC090 | 560 | 480 | 120 | 22 | 19 | 4.75 | 1.1 (2.4) | 692 | 2180 | 12.8 | 201 |
| IMC100 | 560 | 480 | 240 | 22 | 19 | 9.5 | 1.3 (2.9) | 692 | 2180 | 6 | 201 |
| IMC110 | 560 | 480 | 480 | 22 | 19 | 19 | 1.8 (4.0) | 692 | 2180 | 6 | 201 |
| IMC120 | 560 | 960 | 120 | 38 | 22 | 4.75 | 1.9 (4.2) | 737 | 2470 | 13.8 | 201 |
| IMC130 | 560 | 960 | 240 | 38 | 22 | 9.5 | 2.7 (5.9) | 1179 | 2800 | 15.2 | 201 |
| IMC140 | 560 | 960 | 480 | 38 | 22 | 19 | 3.3 (7.3) | 1074 | 2500 | 14.2 | 201 |
| IMC150 IMC160 | 1120 1120 | 480 480 | 120 240 | 44 44 | 19 19 | 4.75 9.5 | 1.7 (3.7) 2.4 (5.3) | 952 1102 | 2470 2500 | 13.8 14.2 | 201 201 |
| IMC170 | 1120 | 480 | 480 | 44 | 19 | 19 | 3.3 (7.3) | 1102 | 2500 | 14.2 | 201 |
| IMC180 | 1120 | 960 | 240 | 44 | 38 | 9.5 | 7.6 (15) | 1815 | 3800 | 19.5 | 201 |
| IMC190 | 1120 | 960 | 480 | 44 | 38 | 19 | 9.2 (20.2) | 1815 | 3800 | 19.5 | 201 |
| IMC200 | 1120 | 960 | 960 | 44 | 38 | 38 | 8.3 (18.3) | 1010 | 2500 | 14.2 | 201 |

Tolerance: Exterior dimensions must be maintained to +0.0 and -5.0mm (+0" and -0.2").

* Note: IMC011/031 are for Hardware and very small parts only, and consist of base + lid.

# Recommended max. loading = 30kg. (62lbs)

| Carton Weight | Weight Disc |  | Handles |
| --- | --- | --- | --- |
| Up to 12kg (26lbs) | Red discs |  | O |  | No handles |
| Up to 30kg (66lbs) | Yellow discs |  | O |  | 2 handles |
| Up to 60kg (132lbs) | Green discs |  | O |  | 4 handles |
| Specials and above 60kg | Blue discs |  | O |  | On Pallet Base |

Conversion Factors: 	1" = 25.4mm 	1kg 	=  2.2lbs

3.3 IMC Carton Selection Process

To establish the most suitable container from the Ford IMC Container Range (see Section 3.2), follow the flow chart shown opposite.  The overall process can be summarised as follows:

1. Does the part fit into a manually handled IMC carton?

(i) 	Establish the smallest carton (see Section 3.2) into which the part fits, and fill the carton fully.

(ii) 	Based on current production volumes, ensure that the carton holds a minimum of 1

hours' stock. If not, investigate the next largest carton. (iii) 	Ensure the final pack does not exceed 12Kg.

(iv) 	If the gross weight is greater than 12 Kg or no small container is suitable, investigate the larger carton range (IMC120 upwards).

2.  Is the part unsuitable for a manually handled IMC carton?

(A)  Trim and Final Assembly Parts:

(i) 	Starting with the IMC 120, establish the smallest IMC carton into which the part fits, then fill the container fully.

(ii) 	Based on current production volumes, ensure that the carton holds a minimum of 1 hours' stock and a maximum of 8 hours stock.   If not, investigate the next largest carton.

(iii) 	Ensure the full unit load (including pallet base) does not exceed 500Kg  (1100 lbs).   If the gross weight exceeds 500Kg contact  Packaging Engineering, for investigation into a unique/special container.

(iv) 	If  the  part  meets  all  criteria,  but  has  a  poor  pack  density,  contact  Packaging

Engineering for further advice.

(B)	Metal Stamping and Body Parts

(i) 	If  the  part  requires  a  special  rack,  contact  IEO Packaging  Engineering  in Ford

Cologne, to establish special expendable packaging.

(ii) 	If part is suitable for a standard IMC carton, proceed as above [Section 3.3 (A)]

.

a)  Consider the DO 'S and DO  NOT S before finalising your pack proposals (see

Section 3.4).

b)  Advise Packaging Engineering of your provisional packaging solution by e-mailing a copy of the 1121E - (see Section 3.1).

c)  Packaging Engineering - IEO will then provide provisional approval (assuming pack spec. is acceptable).

d)  Suppliers must then ensure that all shipments are made in line with the IMC Carton User

Guide (see section 3.6)

e)  Complete the final checklist to ensure that all steps have been covered

f) 	Final packaging approval will be given after production shipments have been audited

3.3.1 Packaging Costs

Packaging costs must be identified and integrated as part of your piece price at the quotation stage, and can only be agreed by Purchase (your commodity buyer).   Confirmation of an 1121E advises that your packaging proposals are acceptable, and does not infer or imply acceptance or agreement of any associated costs with that packaging.

3.3.2 IMC Carton Selection Flowchart

3.2E.1 Export Container Selection

Flowchart

Select the part

in question

Will the part fit

into a hand-held 	NO IMC?

YES

Is the part

supplied to Trim & 	NO Assembly plants?

YES

Is the part supplied to Metal Stamping & Body Construction plants?

YES

Select the smallest available  IMC into which the part fits

Will the part fit 	NO

into an IMC120?

Is the psrt a 	NO

standard EP part?

YES

YES

Fill the IMC with as many parts as possible

Select the next largest IMC

Fill the IMC with as many parts as possible

Select the next largest IMC

Fill the  IMC carton with as many parts as possible

Is the IMC within t

12kg weight limit?

NO

YES

Is theIMC within the

500kg weight limit? 	NO

Is the IMC

within the 1000kg 	NO

weight limit?

YES

Is a larger IMC

available? 	NO

YES

YES

Does the IMC hold more

than 30 minutes' worth of 	NO

stock?

YES

Does the IMC hold less

than 8 hours' worth of 	NO

stock?

YES

Does the IMC carton

hold less  than 8 hours' 	NO

worth of stock?

YES

Is the IMC filled to an optimum

level  (>95%), considering  the 	NO

part details?

Is the IMC filled to an

optimum  level  (>95%), 	NO

considering  the part details?

Is theIMC carton filled to an optimum  level  (>95%),

considering  the part 	NO

details?

YES

YES

Advise the packaging contact at Ford Packaging Engineering, obtain approval and provide packaging specification documentation

YES

Contact Ford Packaging Engineering  for involvement

Ensure all part shipments are sent in approved packaging

Contact Ford Packaging Engineering  for investigation into special container types

3.4.	DO's

DO use corrosion inhibiting materials (e.g. VCI products, etc.) where rusting i s a risk  For other components use the appropriate product quality protection material,  as  required;  e.g.  bubble  wrap,  static-proof  bags,  etc.	Although Packaging Engineering will provide advice, the responsibility for ensuring part protection and quality remains with the supplier.

DO ensure that you use only IMC modular cartons and pallets to the exact specification - this is a fully integrated system that requires each element to meet its specification.

DO ensure that you utilise the maximum cube of the carton - if utilisation is less than 95% try a smaller carton, if available from supplied table.

DO ensure quantity of handles fitted is suitable for the pack weight (see specification)

DO inform Packaging Engineering via the EU1121 form if parts are temperature sensitive. (Temperatures over 70  C can be reached during transport to some destinations).

DO monitor the effect of engineering changes on packaging and submit a new

EU1121 one month prior to any packaging change.

DO select reliable suppliers to provide pallets, stickers and cartons - if you need assistance Ford has approved companies that currently stock IMC boxes. Please contact your local Packaging Engineering IEO Helpline to obtain contact information.

DO ensure your labelling conforms to Fo rd Guidelines.

DO ensure that weight identification discs are displayed (recommended disc size 50 mm diameter). Discs may be stickers or similar markings e.g. stamp, marker etc.

DO ensure that all cartons have the appropriate ISO-Modular Carton Number printed on two adjacent sides. See Example:

IMC100

(ISO-Modular Carton Number)	(Weight Identification Disc 50mm dia.)

3.5	DO NOTS

DO  NOT use a carton that is not specified in  Section 3.2 - no exceptions are permitted without prior written approval from Packaging Engineering

DO NOT allow your product quality to be compromised due to inadequate packaging - zero defect is the required norm.

DO  NOT pack different parts within the same carton  - only one part number per carton is allowed. The packaging of “handed” pairs may be considered, after evaluation by Packaging Engineering.

DO NOT use additional aids to strengthen IMC cartons (e.g. belly bands, etc).  Heavy unit  loads  that  require  the  use  of  corner  posts  must  be  specifically  approved  by Packaging Engineering.

DO  NOT allow cartons to overhang pallets. Ensure they are correctly stacked and positioned.

DO NOT use staples for carton closure (top or bottom). Staples may damage both the parts and the operators during the unload operation.

DO NOT ship pyramid loads - these are not acceptable under any circumstances.

DO NOT use horizontal banding to improve load stability – IMC board specification is sufficiently strong.

DO  NOT use steel banding to secure loads  - use plastic banding  and/or stretch wrapping.

DO   NOT  use   packaging   material   that   cannot   be   re-cycled,   or  could   be environmentally harmful after disposal.

DO NOT modify modular boxes. Example 1: do not cut side seams to make a box smaller.  Example 2: do not telescope two boxes together to create a larger box.

DO NOT exceed 300 parts per carton unless the smallest IMC in Section 3.2  has been selected,  in which case the carton should be filled to capacity irrespective  of quantity.

DO  NOT allow the maximum weight of a unit load including pallet base to exceed

500kg (1,100lbs) without Packaging Engineering approval. Those that are approved must be marked "BOTTOM LOAD ONLY" on two adjacent sides of the carton.

3.6 	IMC Carton User Guide

Once the optimum export carton has been selected and approved for your part, it is essential that you prepare and consolidate the cartons in the correct manner for shipment:

Unit loads must be constructed in accordance with the guidelines in Section 1.10.

Pallet bases must conform to the specification in Section 3.8.

Each carton must at least be labelled with Ford standard Odette or AIAG

labels on two adjacent sides. For IMC cartons where height is less than

120mm (4.75”) the chosen label data format must be used but the label must

be reduced to fit onto the side of the carton.

Maximum height of any unit load must not exceed 1100mm (43") unless approved by Packaging Engineering.

If you supply more than one part number to Export Markets, mixed loads of various cartons on a single pallet are permissible to achieve a realistic unit load, provided they are for the same plant destination.

Carton flaps must be completely sealed with tape or spot gluing.

All modular carton loads must be secured to the pallet with plastic banding and/or clear plastic stretch wrap. Under no circumstances should steel banding be used. Nailing, stapling or gluing is not acceptable.

3.6.1 Loading Cartons to Pallet Base

Carton alignment:

IMC150

R

IMC100

G

G

IMC060

R 	R

Y

G 	G

IMC060

3.6.2 Loading Cartons to Base by IMC Type

Mixed unit loads of different part numbers and/or carton sizes ARE acceptable, the modular carton design allowing all cartons to be inter-stacked. Homogeneous unit loads are shown simply to illustrate relative carton size and orientation on the ISO-Modular pallet.

IMC 010/011	IMC 020	IMC 030/031	IMC 040

IMC 050	IMC 060	IMC 070	IMC 080

IMC 090	IMC 100	IMC 110	IMC 120

IMC 130	IMC 140	IMC 150	IMC 160

IMC 170	IMC 180	IMC 190	IMC 200

3.8 	ISO Modular Pallet Dimensions

All export market shipments must conform to the 980mm(39”) x 1140mm (45”) full perimeter pallet specification below, designed specifically for ISO container shipments. Alternate dimensions are NOT acceptable . Corrugated pallets are not acceptable unless approved by Packaging Engineering.

EXPORT SHIPMENT PALLET BASE SPECIFICATION

1140mm (45in) 	3

16

150 TYP

520 	520

5

220

1

980mm (39in)

220

2

220

220

100

3

4 	100 TYP

DETAIL

16

3 	3 	3

75 - 95

100 TYP

16

5

| 5 | Softwood |  | 1140 | 100 | 16 | 7 |
| --- | --- | --- | --- | --- | --- | --- |
| 4 | Softwood |  | 980 | 100 | 16 | 3 |
| 3 | Softwood |  | 150 | 100 | 75 | 6 |
| 2 | Softwood |  | 100 | 100 | 75 | 3 |
| 1 | Softwood |  | 780 | 100 | 16 | 3 |
| ITEM | DESCRIPTI | LENGTWHIDT HEIGH | TQTY. |

ALL DIMENSIONS IN MM ASSEMBLY TOLERANCE +/- 3MM

DETAIL

THIRD ANGLE PROJECTION	 BOTTOM OF PALLET MUST BE FLAT

NO STEPS ALLOWED AT CORNERS

* ALL MATERIAL MUST CONFORM TO PROCEDURE KDP-p-3

APPENDICES

1. Glossary of Terms

2.  EU1121 - Packaging Data Form VO Production

3.  Packaging Non-Conformance Form

4.  Transport Mode Dimensions

5. Re-cycling and Plastics Identification Symbols

6.  Durable Insert Standard

Appendix 1: Glossary of Terms

| CMMS3 | “Common Material Management System”. Global Logistics / Packaging Database (replaced NewPac) |
| --- | --- |
| Cube Utilisation | A measure of efficiency of space used within transport trailers |
| Dunnage | Packing material within the container used for part protection |
| Durable Packaging | Packaging material designed to last a minimum of 5 years |
| Expendable Packaging | Packaging material designed to be used for a single trip only |
| FLC 1210 | Folding Large Container - Unit Load sized plastic container with drop- down access doors, which can be folded for return journey |
| FSC 1206 | Folding Small Container - Half-Height Unit Load sized plastic container without drop-down access doors, which can be folded for return journey |
| FPS | "Ford Production System" - World Class Lean Manufacturing Strategy |
| IEO | “International Export Operation” - new name for KD Operations |
| ILVS | “In-Line Vehicle Sequencing” - Parts shipped to point of use in vehicle build order |
| IMC | “ISO Modular Carton” - Standard Cartons used for export shipping |
| ISO14001 | Environmental Quality Standard |
| JIT | “Just In Time” - Scheduled time-slot delivery system |
| KD | "Knock-Down" - Now replaced by "International Export Operation" (IEO) |
| KLT | “Klein Ladungs Traeger”. A range of plastic modular containers |
| Master Label | Label used on unit load of modular containers, when all parts are the same |
| Mixed Load Label | Label used on unit load of modular containers with mixed part numbers |
| MS&B | “Metal Stamping and Body Construction”. Vehicle operations plants |
| Odette Label | European Automotive Industry Standard Label |
| QS9000 | Automotive Quality Standard |
| PTA | “Paint, Trim and Assembly”. Vehicle operations plants |
| Shipping Trials | Test shipment completed with the receiving plant to ensure packaging is acceptable |
| SMF | “Synchronous Material Flow” - Optimum material flow to support Ford Production System |
| Special Container | Container designed with unique fittings to suit a particular part |
| Third Party Hire | Container leasing & management from external supplier |
| VCI | Vapour Corrosion Inhibiting - Coating or material to prevent rust forming on parts |
| Unit Load | Typically 1200mm x 1000mm x 1000mm packaging unit |
| Weight - Gross | Total weight of container and contents including dunnage |
| Weight - Net | Weight of parts in container (excluding container and dunnage weight) |
| Weight - Tare | Weight of empty container |

Ford Motor Company, Vehicle Operations / IEO

European Production / Export Part  Packaging Data Form

| Part No. | Prefix | Base | Suffix |
| --- | --- | --- | --- |
| Part Name : |  | Plant Code(s) |
| Pieces per day |  |  |  |
| See reverse side for instructions relating to the numbered fields |  |

APPENDIX 2:  EU1121 Packaging Data Form

Supplier Details	Ford Part Number

| Ford Supplier Code: |  | Today's Date: |  |
| --- | --- | --- | --- |
| Supplier Name & |  |
| Address |  |
| Contact Person |  | E-mail |  |
| Phone Number | Fax Number: |  |

| 1 | Packaging type |  |
| --- | --- | --- |
| 2 | Effective Date |  |
| 3 | Confirm code |  |
| 4 | Container Type or Number |  |
| 5 | Pieces Per Container |  |
| 6 | Length (cm) |  |
| 7 | Width (cm) |  |
| 8 | Height (cm) |  |
| 9 | Tare Weight (kg) |  |
| 10 | Piece Weight (kg) |  |
| 11 | Gross Weight (kg) |  |
|  | Expendable Packaging cost (per piece) | Durable Packaging cost (per piece) | Currency Code |
| 12 |  |  |  |
| Carton Details (for expendable type COP & PTP only) |
| 13 | Pieces Per Carton |  |
| 14 | Cartons per Layer |  |
| 15 | Layers per Pallet |  |
| 16 | Length (cm) |  |
| 17 | Width (cm) |  |
| 18 | Height (cm) |  |

Photo / Sketch of packaging	Packaging Data

| Please display a picture here if :- 1. The part is an FLC or FSC container. 2. The part is packed in a KLT with internal packaging, either durable or expendable 3. The part is in a "special" container - i.e. a non-standard returnable or supplier owned container 4. The part is in an IMC or export carton with internal packaging or corrosion protection. The picture must clearly show part orientation within the container, and internal packaging details must be recorded in the boxes below with additional details in Packaging Description if necessary. |
| --- |
| 20 Durable Inserts | 21 Expendable Inserts (insert quantity per container) | Cells |  |
| Qty per Container |  | Foam |  | Paper |  | PE Bags |  | Oil |  |
| Type/Ref. Number |  | Layer Pads |  | Bubble Wrap |  | Polystryrene |  | VCI |  |
| 22 Indicate If: | Hazardous Mat'l (Y/N) |  | Temperature Sensitive (Y/N) |  | Weight Disc (Y/N) |  |

| 23 | Signed | Name (Printed) | Date |
| --- | --- | --- | --- |
| Supplier |  |  |  |
| Ford Packaging |  |  |  |
| Production |  |  |  |
| Quality |  |  |  |
| SMF |  |  |  |

| European Prod. |  |  |  |
| --- | --- | --- | --- |
|  | or FAX |  |  |  |
| Export |  | eu1121e@ford.com |  |
|  | or FAX | 44 (0)1708 672211 |  |

Approvals	Return Form to:	Packaging Description (complete  if internal packaging  used) OR

Reason for non-IMC (Export only)

24

Version: January 2002

Form number: EU 1121C	Registered in England : No. 235446 Registered Office : Eagle Way, BRENTWOOD, Essex, CM13 3BW, UK	This form may be photocopied

Appendix 3: Packaging Non-Conformance Form

PACKAGING NON-CONFORMANCE

| Suppliers/Carriers or Shipping Address Suppliers Code No: | Receiving Plant: |
| --- | --- |
|  | Plant Contact Person: |
|  | Phone No: | Fax No: |
|  | Location Code: | Date of Issue: |
|  | Reference No: | Date Received: |
|  | Part No: | Trailer No: |

The following deviation from the agreed packaging has been identified. Please refer to  Packaging Requirements Brochure EU 1750A.

You must respond to the plant contact above within 48 hours and arrange correction within 20 days

INCORRECT PACKAGING 	KLT 	COMMENTS

TYPE 	3214 	4314 	4328 	6428 	FLC 	SPE C

EXP

APPROVED PACKAGING TYPE

PACKAGING TYPE SUPPLIED

General Issues 	KLT Specific Issues

lid

Wrong part quantity for container 	Load unit not supplied with specified base or

Parts are not packaged correctly 	Load unit incorrectly assembled or secured

Container is not clean 	Mixed load unit incorrectly labeled

Container is not in good repair 	Weight is greater than 15kg

Container is labeled incorrectly

Issues

FLC Specific Issues	Special Durable / Expendable / Other

FLC net weight exceeds 500kg requirement 	Container does not conform to

requirements.

Container sides are not correctly erected / secure

Further Comments

E 	EU 2714 	Reported By: 	Authorized By

EU1750  April 2000

Appendix 4:	Transport Mode Dimensions

(Internal dimensions are indicative - for absolute dimensions consul

Mega Trailer

Length  13.52	Max payload 24T Width	2.42	Volume:	96.81m3

Height  2.99	]	OOO

SuperCube Top Deck	Lower Deck Length  3.45	Length  9.01

Width	2.30	Width	2.3	Max payload: 24T

Height  2.51	Height   3.05	Volume:83m3	]	OOO

HTM

Length  13.60	Max payload:24T Width	2.50	Volume:

Height  2.8 or 2.35	]	OOO

12M

Length  12.20	Max payload:20T Width	2.42	Volume:	71m3

Height  2.42	]	OO

Tautliner/Curtainsider

Length  13.30	Max payload 23T	EXEL Logistics

Width	2.40	Volume:	105m3

Height  3.35	]	OOO

Mega TIR

Length  13.60	Max payload:22T	norfolk line

Width	2.50	Volume:	104m3

Height  2.97	]	OOO

13.6 Tilt TIR	FERRYLINE

Length  13.45	Max payload 22.5T Width	2.44	Volume:	84m3

Height  2.58	]	OOO

|  | CARGOWAGO | N |
| --- | --- | --- |

Rail Wagon

Length  13.94	Max payload:28T Width	2.62	Volume:	84.7m3

Height  2.01	OO	OO

| Length | 13.37 | Max payload 20T |
| --- | --- | --- |
| Width | 2.44 | Volume: | 73.08m3 |
| Height | 2.24 |  |  |

SwapBody

Transfesa

Ford Motor Company  - Vehicle Operations European Packaging Guidelines

APPENDIX 5: Recycling and Plastics Identification Symbols

Sources:

Recycling symbols are those proposed by European Union

Plastics Identification codes are those devised by the Society of

Plastics Industry (SPI) in USA

1. Polyethylene Terephthalate

2. High Density Polyethylene

3. Polyvinyl Chloride (PVC)

4. Low Density Polyethylene

5. Polypropylene

6. Polystyrene

7. Other

EU1750  April 2000

Appendix 6

DURABLE INSERT

& EXTENDED

CONTAINER STANDARD

APRIL 2002

MH&PE Standard Procedure

Contents

Introduction

Development Process

1.  Insert/Extended Container Requirement

2.  Funding

3.  Development

4.  Identification

5.  Return Process

Operating Process

A). Supplier Responsibilities

B). Ford VO Location Responsibilities

C). Third Party Container Supplier Responsibilities

Appendices

a)  Identification Label

b) Completed Return Specification

Additional Return Specification Information (optional)

c)  Pallet Return Label d) Tracking Form

e)  Durable Insert Follow-Up Process

f)	Schematic Timing

Introduction

The use of 100% durable packaging is a long-term aim of Ford motor Company, to support both greening and environmental objectives.    The introduction of standard durable outer packaging for all Ford European plants is now complete, and the emphasis in future will be on providing economic durable internal packaging, and non-standard sized (extended) durable containers.

Unlike  standard  containers,  which  are  pooled  and  can  be  used  by  any  supplier, inserts and extended containers are dedicated to specific commodities and hence suppliers. The smooth flow of inserts and extended containers between the supplier and Ford must be recognised as an integral part of the production process, and a robust process for their return must be established if progress towards this objective is to be achieved.

The purpose of this standard is to support this objective by:

ensuring that durable inserts/extended containers meet both supplier and Ford requirements

enabling all affected parties to recognise and know how to handle durable inserts/extended containers.

ensuring that a return process is established before durable inserts/extended containers are introduced.

Application of this standard will provide a common approach for:

Identifying suitable products for durable inserts/extended containers. Funding of durable inserts/extended containers.

Timing, development, identification, and approval of durable inserts/extended containers.

Establishing a robust return process to ensure inserts/extended containers are returned to the correct source supplier on a timely basis.

Operating and follow-up procedures

Adherence to this standard will ensure that your durable inserts/extended containers will be used and returned by the receiving plant, and any operational concerns can be quickly identified and addressed.

1)  Insert/Extended Container Requirement

The component supplier and Ford MH&PE agree in principle that a durable insert/extended container is needed, to meet quality, ergonomic, or cost reduction requirements.

2) 	Funding

For  inserts,  the  supplier  provides  MH&PE  with  cost  breakdown  for  both durable   and   expendable   insert   alternatives,   including   potential   savings (avoiding use of cardboard, improved density) plus tooling and investment costs.

For extended containers, the supplier provides details of the best standard container option together with any specific quality concerns.

MH&PE complete cost analysis of options, including material savings and freight costs for both inbound and return shipments.

If  cost analysis meets acceptance  criteria,  MH&PE  advise  Purchase, user plant and supplier.

If costs are already included in piece price then supplier proceeds with development in conjunction with MH&PE.

If costs are not included in piece price then supplier/Purchase negotiate to confirm funding arrangements before development commences.

3)  Development

Supplier discusses requirements with MH&PE and receiving plant to establish insert/extended container type, ergonomics, and any special requirements. Items to be agreed include:

Type of insert/material

Container size and any internal separation

Component orientation

Method of handling

Approximate	size	and	weight.	Please	note	that	maximum	external dimensions for inserts to be used with an FLC container must not exceed

1100 x 890 – this is to allow for worst case manufacturing tolerances on the

side walls of the (FLC) container.

Identification method, including Ford reference number

Method of return – collapse ratio for inserts

Any special requirements

Supplier to establish timing plan (see Appendix (f)) to meet program/plant requirements - to be /agreed by MH&PE and receiving plant.

Development to take place with support of MH&PE.

Production  level  prototype  pack  to  be  trialled  to  the  receiving  plant(s)  for acceptance by MH&PE and affected receiving plant departments, including:

Packaging Engineering

MPL (local plant and central logistics) Production

Quality Safety FPS/Layout

Once	plant	acceptance	has	been	obtained,	main	production	of	the inserts/extended containers can commence.

Inserts/extended	containers	must	be	manufactured	and	identified	in accordance with this standard.

4)  Identification

1. Insert/extended container identification is required for operators to identify empty inserts/containers in transit (inbound inserts are identified by the product in the pallet).

2. Identification to be as follows:

Each insert must be individually identified on 2 sides.  This is to ensure that if a pallet lid is raised for inspection of the contents, the identifying label can be seen irrespective of which side the pallet is viewed from.   If inserts are to be returned inverted, then the labels should be on the underside of the inserts.

4. Extended containers to be identified on two sides

3. Labelling/identification (Appendix (a)) must include the following: Part description (eg. cluster/radiator etc)

Model line (eg. Mondeo/Fiesta/Focus etc) Return location (Supplier name and town) Ford GSDB code (5-digit supplier code)

4. Inserts/extended containers may be clearly printed with contrasting colour if size allows, or coloured self-adhesive labels may be applied.

5. Labelling must be clearly legible.

(NB. Embossed information on the surface of the insert is not adequate for identification

purposes, and if used should be considered as supplementary identification only).

6. Labelling must be approved by MH&PE (Aveley 20/220) and the user plant.

7. Poke Yoke principles to be agreed with user plant and included if appropriate

(failsafe features that help prevent incorrect use of the equipment).

5) Return Process

Not later than two months prior to introduction the following items must be provided to MH&PE:

1.  Completed EU1121 Packaging Form with photographs (Packaging Guidelines Appendix 2) showing part orientation/location in the insert/extended container, including any instructions for loading/unloading.

2. Completed Return Specifications (Appendix (b)) showing: Method of collapsing/nesting inserts Location/orientation within the container

Quantity per container

Any special instructions

3.  Completed return Label (Appendix (c))

4.  Completed Tracking Form (Appendix (d))

5.  Routing for both inbound and return shipments must be defined at the procurement stage, as this will affect the number of inserts to be purchased. Routing should identify:

Direct or indirect shipments, both inbound and return If indirect, actual routing through logistics suppliers Frequency of shipments

Number of days float associated with each of the above. Float requirements at the supplier.

Float requirements at the user plant.

Float requirements for return organisation

6.  Details of calculation showing number of inserts purchased.

(NB.  Ford policy is to provide sufficient packaging to ship the finished product from the supplier to the user plant, and return.  For the Supplier, this includes one day of inserts waiting to be used, one day in production, and a one day shipping bank awaiting collection.  It does not include Supplier in-process requirements, batch

production requirements, or stock piling.  Deviations from this policy must be agreed between MH&PE, Purchase, and the user plant).

7. One week prior to first shipment supplier to advise receiving plant and

MH&PE of first shipment date.

Operating Process

The following procedures are recommended to suppliers and Ford VO locations to ensure that the movement of inserts/extended containers operates smoothly and any concerns can be identified and addressed promptly.

A). Supplier Responsibilities

a)  Inserts/extended containers must be developed and supplied in accordance with this standard.

b)  The supplier must provide a timing program in line with Appendix (f) at the start of the program.

c)  Supplier must provide the following at least two months before inser/container introduction:

EU1121 Packing Specification Form (Packaging Guide - Appendix 2) Insert/extended container Return Specifications (Appendix (b)) Pallet labels (Appendix (c)):

Labels must be in this format for identification and tracking purposes.

Local language identification can be inserted on a middle line to aid recognition. Labels to be provided by the source location (supplier) by e-mail - local supervision will print off the labels as required and ensure availability to the insert/extended container consolidation area.

Completed Tracking Sheets (Section A Insert Details and Section B Quantity Details only to be completed by supplier) for each  Ford VO destination that the inserts are shipped to (Appendix (d)).

d) 	Supplier to designate insert/extended container ‘Champion’, to log receipts and follow- up delinquencies.

e) 	Supplier 'Champion' to log inserts/extended containers received, by quantity and user location:

The description (e.g. ZD - Orange Radiator) identifies the VO location and insert

/extended container type.  By recording returns and the returning VO location on

a daily basis (e.g. on a spreadsheet) any delinquencies in the return process can be identified and addressed quickly.

For durable inserts only:

Having previously specified the quantity of inserts per container (from Return Specification and Tracking Sheet), the number of inserts can be determined and added to the available inventory.

The number of FLC’s recorded can be collated daily and the quantity subtracted from the FLC order quantity - this will vary by source location according to their arrangement with the third party container supplier.:

f) 		In the event of an identified delinquency in the return process, source plant to apply the ‘Durable Insert/Stretch Container Follow Up Process’  - Appendix (e).

B). Ford VO Location Responsibilities

1. Ensure that return packing specifications are available (from supplier) and displayed to affected operators.

2. Pallet labels and Tracking Sheets (from supplier) are available prior to insert introduction.

3. VO user location to pack inserts/extended containers according to the return packing specification, for return:

On the production line or in the satellite plant or in the EPC

using Ford or contract labour according to local conditions and processes.

4. When pack is complete, dust cover is fitted and two off specified labels are inserted, one to each of the two label holders on the FLC (inserts), in two adjacent label holders for extended containers.

5. Local supervision to ensure that specified return labels are available to operators.

6. Ford responsible EPC personnel (Ford or contractor according to local conditions) to advise 3rd Party EPC Logistics office personnel by 8.00am each morning of the type and number of pallets of each insert/extended container ready to ship.

C). 3rd Party Container Provider EPC Logistics Office

Responsibilities

1).  Once per day, the 3rd   party container supplier will raise shipping documents for each destination and arrange transport with Ford Fleet via the 3rd   party container supplier logistics office in Hurth.

Shipping (5427x) document will contain full description of inserts/extended containers (e.g. “ ZD - Orange Radiator Inserts”) as it appears on the return label.

Shipper will be addressed to destination (supplier/source location) - this will enable consignments of inserts/extended containers to be tracked via traffic.

It will also enable the source plant to monitor returns by type and quantity from specific user (VO) locations.

2). The third party container supplier will log the documentation number (5427x) plus the trailer number (or vehicle registration number):

This will allow both inserts and  containers to be traced through Traffic in the normal way, irrespective of source or destination.

For durable inserts, using the 5427x document enables the source location to quantify the additional FLC’s arriving in plant, and adjust their FLC call-off accordingly.

APPENDICES

a) Identification Label

b) Completed Return Specification

Additional Return Specification Information (optional)

c) Pallet Return Label d) Tracking Form

e) Durable Insert/Extended Container Follow-Up Process f)  Schematic Timing

APPENDIX (a)

Insert/Extended Container

Identification Label

Suitable for : o	extended containers o	vacuum formed trays

o	foam/moulded inserts

o	any insert where there is insufficient area

to paint or print a contrasting colour identification

AME Drawing Number	Model	Part Description

FE10766 MONDEO RADIATOR MODULE RETURN TO :

0114A - VISTEON BASILDON UK

Supplier 5-digit GSDB Code  Supplier name	Town	Country

Note! For durable inserts, two labels per insert should be provided. They should be positioned such that if the container lid is lifted to inspect the container contents, at least one label is clearly visible.

Genk - Return Specification for CD132 buckle Layerpads

CD132 Layerpad - buckles from ABC Polska

Only one type of layerpad in each FLC.

Make sure that there are

20 empty layerpads in each FLC.

Load trays Up Side Down into FLC

Empty Layerpad

Identification Label = White

APPENDIX (b)

For any further informations don’t  hesitate to contact:

Joe Bloggs

ABC Polska, Czestochowa, POLAND Tel: #48 34123 4567

Fax:#48 34123 4568

E-mail: jbloggs@abc.com

CHEP FLC 1210

APPENDIX (c)

2C	-	Mondeo

Cluster

20	inserts

Return to Enfield

UK	- 6620A

2C	-	Mondeo

Cluster

20	inserts

Return to Enfield

UK	- 6620A

Ford Motor Company, Vehicle Operations

Durable Insert/Extended Container Tracking Form

| Supplier Name: |  | User Plant: |  |
| --- | --- | --- | --- |
| Supplier Code: |  | Model Line: |  |
| Supplier contact: |  | Part Number: |  |
| Supplier 'Phone: |  | Description: |  |

| DPV: |  | Durable Inserts | Extended Containers |
| --- | --- | --- | --- |
| Floats: Supplier |  | 18 | Type: |  | Type: |  |
| Transit Inbound |  | 19 | Ford Ref. Number: |  | Ford Ref. Number: |  |
| Transit Return |  | 20 | Parts/Pack: |  | Parts/Pack: |  |
| Ford |  | 21 | Tare weight: |  | Tare Weight: |  |
| EPC |  | 22 | Inserts/Container Inbound: |  | Container Dims L*W*H cms: |  |
| Quantity Purchased |  | 23 | Inserts/Container Return: |  | Containers/UL: |  |
| Standard Labels Complete | Yes / No | 24 | UL/day Inbound: |  | UL/day Inbound: |  |
| Return Specs Complete | Yes / No | 25 | UL/day Return: |  | UL/day Return: |  |

A Supplier /Product Details (Supplier Completion)

APPENDIX (d)

| 1 |  | 5 |
| --- | --- | --- |
| 2 |  | 6 |
| 3 |  | 7 |
| 4 |  | 8 |
| B Quantity Details (Supplier Completion) |  |  |
| 9 |  |  |
| 10 |  | 26 |
| 11 |  | 27 |
| 12 |  | 28 |
| 13 |  | 29 |
| 14 |  | 30 |
| 15 |  | 31 |
| 16 |  | 32 |
| 17 |  | 33 |
| C Tracking Sequence (Plant Completion) | As Applicable |  |

| Operation | Responsibility | Location | Frequency (days) | Duration (days) | Telephone Number/Comments |
| --- | --- | --- | --- | --- | --- |
| Potential events required to facilitate return of inserts/containers to supplier | Supervisors/Operators name | Plant location (grid reference) or Supplier Park location or Logistics Supplier name | How often the event occurs, in days | How long the event typically takes, in days | Telephone number to contact in the event of concerns arising |
| In-Plant Routing: |  |  |  |  |  |
| Specs displayed? | Yes / No |  |  |  |  |
| Line Location: |  |  |  |  |  |
| Market Place: |  |  |  |  |  |
| Empty return location: |  |  |  |  |  |
| Re-pack/Consolidation: |  |  |  |  |  |
| Milk round collection: |  |  |  |  |  |
| Return to EPC Compound: |  |  |  |  |  |
| EPC advised of empties: |  |  |  |  |  |

34

35

36

37

38

39

40

41

42  Logistics Co-ordinator:

43 	Traffic advised:

44 	Freight organised:

Freight Functions:

45 	Traffic collect inserts:

46 	Freight movement 1:

47 	Consolidator 1:

48 	Freight movement 2:

49 	Consolidator 2:

50 	Freight movement 3:

Supplier Functions:

51 	Delivery receipt:

Total: 	days

D

| Concurrence | Name (printed) | Signature | Date | Return To: Ford Motor Company Limited AME MH&PE GB-20/220 Arisdale Avenue South Ockendon Essex RM15 5TW Tel / Fax : *44 (0)1708 672156 / 211 |
| --- | --- | --- | --- | --- |
| MH&PE: |  |  |  |  |
| Plant: |  |  |  |  |
| Supplier: |  |  |  |  |
| Traffic: |  |  |  |  |
| LLP Co-ordinator |  |  |  |  |

52

53

54

55

56

AME MH1E GB 20/220

October 2000

Registered in England: No. 235446   Registered Office : Brentwood, Essex,  CM13 3BW, UK

APPENDIX (e)

Durable Insert/Stretch Container Follow-Up Process

In the event of concern regarding return of inserts/extended containers, use the

Tracking Form to:

1.  Identify the VO location causing concern - this will be apparent as labels carry the VO plant code e.g. ZF, ZS, 1Y, 3C, 2C, V5. Inserts will not be arriving from the location causing concern.

2.  Contact the appropriate 3rd party EPC or Supplier Park contact.

3.  Ask if the particular insert /extended container has been shipped within past

24 hours.

4.  If yes, ask the document number and trailer number - go to item 6.

5.  If no, contact the plant MP&L Manager to establish why inserts/containers are not being returned.

(Note! 3rd Party do not control insert/extended container movement  - they record

information supplied by Ford responsible EPC staff to facilitate tracking).

6.  If inserts/containers are coming from a domestic location (i.e. within FoB, FoS, or FoG) contact traffic.

7.  Give them the trailer number and advice note number.

8.  They will advise trailer location and estimated time of arrival.

9.  If inserts/extended containers are coming from abroad, contact the LLP Hays storage for inserts/containers coming into FoB locations

Antriss & Schneider for inserts/containers coming into FoG locations

Transvesa for inserts/containers coming into FoS locations

10. Give them the trailer no. and advice note number.  They will advise if the inserts/containers have come through their area.

11. If yes, they will be able to give an ETA.

12. If no, they will advise the consolidator the material will come from eg.

Inserts/containers coming into FoB from the continent via Hays will be shipped from Transvesa (FoS) or Antriss & Schneider(FoG).

13. Contact the specified consolidator and give them the trailer no. and advice note number.  They will advise if the inserts have come through their area.

.

14. If yes, they will be able to give an ETA.

15.  If no, contact Traffic - under these circumstances 3rd Party have provided the trailer number and advice note number and the trailer cannot be located.

Durable Insert/Extended Container Schematic Timing

Time frame to suit product

Appendix (f)

1 	Initial Supplier Meeting

Collect data/Cost analysis

2 	Confirm Funding

Identify source

3 	Specification Meeting

Confirm design parameters

4 	Provide Quotation

If appropriate

5 	Manufacture Prototype Tools

Produce samples

6 	Review Samples

Plant buy-off/Agree modifications

7 	1PP Shipments

Use Samples for 1PP shipments

8 	Manufacture Final Tools

Produce samples

9 	Submit Documentation

EU1121/Return Specification/Tracking Form/Labels

10 	Review Final Samples

Produce samples

11 	Finalise Production Schedule

To support Job 1 and Launch

12 	Manufacture and Deliver Bulk Production

In- line with schedule

1PP

JOB 1

Key Dates